2008 FIRST Robotics Competition - Inspection Check List

Team No. _____

Inspector________________________________________________

Signature		time/date		printed name and initials

*signature above indicates that the robot has passed inspection

| GENERAL – (testing at the Inspection Station) |
| --- |
| ITEM | PASS | DESCRIPTION | RULE(S) | COMMENTS |
| 1 |  | Size: Must fit in sizing box (28” x 38” x class height), standard bumpers may be removed, robot must be in largest starting config, no bicycle flag, decorations must be present | R11-13, R107-108, R111, R114 |  |
| 2 |  | Weight: Must weigh no more than permitted given robot class | R11 |  |
| 3 |  | Standard Bumpers: must be used, must be 15.0 lbs or less with no heavy spots and must cover at least 2/3 of the robot’s perimeter | R08, R13 |  |
| 4 |  | Bicycle Flag: Must have an appropriate holder with correct installed height - 75” +/- 5”. The flag needs to remain approximately vertical while the robot is in its PLAYING CONFIGURATION (the orientation of the robot beginning sometime soon after the start-of-match and for the remainder of the match). | R16 |  |
| 5 |  | Bill of Material: Attach BOM. Less than $3500 total cost with no individual component over $400. No assembly of modules (total > $400) that is only functional in a single configuration. | R21-26, R35 |  |
| 6 |  | Teams from outside North America: Attach confirming letter if the team has successfully petitioned FIRST for a component exemption | R42 |  |

| GENERAL |
| --- |
| ITEM | PASS | DESCRIPTION | RULE(S) | COMMENTS |
| 7 |  | Safety and Wedges: No sharp protrusions or edges that could harm players, field or game pieces, no entanglement risks, no exposed pinch points, no wedge-shaped robot bases that may potentially affect other robots | R04-R05, R07, R19 |  |
| 8 |  | Energy Sources: No illegal energy sources, battery must be secured | R01 |  |
| 9 |  | Logos: School and sponsor logo and/or name must be clearly visible | R14 |  |
| 10 |  | Team Number: Must be clearly displayed on all 4 sides | R15 |  |
| 11 |  | LED Flasher: Must be used and be clearly visible from the front | R66 |  |
| 12 |  | Interference Mechanisms: Robot cannot include devices or decorations that may interfere with the vision systems of other robots | R03, R20 |  |
| 13 |  | Decorations: Cannot affect match, cannot broadcast using wireless comm w/o clearance from FIRST Engineering, cannot employ 900MHz cameras | R20, R57, R84 |  |
| 14 |  | Team Visibility: Shields, curtains or other devices on the robot cannot obstruct or limit the visibility of other teams’ robots | R02 |  |

| MECHANICAL SYSTEMS |
| --- |
| ITEM | PASS | DESCRIPTION | RULE(S) | COMMENTS |
| 15 |  | Acceptable Mechanical Parts: refer to details in reference material | R10, R35 |  |
| 16 |  | Specifically Prohibited Mechanical Parts: refer to details in reference material, confirm that the robot does not include any of the listed parts, carefully examine the robot for mechanisms that can harm people, other robots or the playing field (including game pieces) | R02, R06, R36, R38-39 |  |
| 17 |  | Motor Modifications: refer to details in reference material, motors can only be modified by machining new mounting holes, modifying output shaft (including removal of gearbox and extraneous items) and altering leadwires | R61 |  |
| 18 |  | Standard Bumpers: refer to requirements in reference material | R08 |  |
| 19 |  | Lap Indicator: must have unobstructed access around the top of the flag holder | R17 |  |

| ELECTRICAL SYSTEMS |
| --- |
| ITEM | PASS | DESCRIPTION | RULE(S) | COMMENTS |
| 20 |  | Acceptable Electrical Parts: refer to details in reference material | R35, R43-44, R58-59, R63-64 |  |
| 21 |  | Specifically Prohibited Electrical Parts: refer to details in reference material, confirm that the robot does not include any of the listed items | R02-R03, R38, R45, R53, R56, R60, R63-64, R82 |  |
| 22 |  | Insulated 12V battery terminals with copper lugs from FCI Burndy bag or similar lugs. Confirm that the battery is securely fastened within the robot. | R50 |  |
| 23 |  | Battery connected to 120A main breaker via Anderson Quick-Disconnect connector. Main breaker and battery ground must be connected to the Rockwell power distribution block for driving breaker panels (refer to the FIRST power distribution diagram). | R46, R50 |  |
| 24 |  | Accessibility: 120A main circuit breaker, distribution breakers and RC are all accessible for inspection. In addition, the RC lights must be visible while standing 3’ from front of the robot while in its STARTING CONFIGURATION. | R50, R72 |  |
| 25 |  | No modifications to Robot Control System (including OI, RC, Victor, Spike, Modems, Batteries, Chargers, AC adapters or 9-pin cables) except DIP switches on OI, user code for RC, Victors can be calibrated and the fuse on the Spike Relay Module for the air compressor (if used) can be replaced with 20A Snap-Action circuit breaker | R67 |  |
| 26 |  | No 12V power, Victor or Spike Outputs or PWM Outputs can be connected to the analog or digital I/O headers on the RC | R76 |  |
| 27 |  | 7.2V NiCad “backup” battery is connected to the Controller and, if desired, to either the custom on-robot charging circuit designed by IFI or similar | R49, R73 |  |
| 28 |  | Wire Size and Color Rules: refer to details in reference material | R46-47, R50, R54, R70-71 |  |
| 29 |  | Either a 20A, 30A or 40A circuit breaker must be used with each Victor | R52, R55 |  |
| 30 |  | 20A circuit breakers must be used to provide power to all Spike Relay Modules, the Air Compressor (if used), Custom Circuits, Additional Electronics and the Robot Controller. Multiple loads may be attached to each Spike Relay Module but only one motor per module is allowed. No other loads may be attached to the Circuit Breakers that provide power to the Robot Controller and Air Compressor. | R52, R55 |  |
| 31 |  | CIM and Fisher Price motors can only be connected to Victor 884 Speed Controllers (they cannot be connected to Spike Relay Modules). Motors can only be driven by one Victor (although a Victor can drive more than 1 motor). | R46, R56, R62 |  |
| 32 |  | Motors (other than Hitec servos and fans) must be wired to Spike Relay Modules or Victor 884 Speed Controllers. Servos must be wired to the RC. Solenoid valves and compressor (if used) must be wired to Spikes. Motors, valves and compressor cannot be wired directly to breakers or other devices for supplying power. | R46, R55, R62 |  |
| 33 |  | The coast/brake headers on Victor 884 Speed Controllers can only be attached to either selection jumpers or digital outputs from the RC | R75 |  |
| 34 |  | Sensor Outputs: Refer to details in reference material. Sensor outputs can only be wired to Robot Controller ports or Custom Circuits. | R03, R53, R64, R80-83 |  |
| 35 |  | Custom Circuits: May only connect to RC ports, sensors or the following outputs – circuit breakers, Victors and Spikes. Small capacitors can be placed across motor leads and resistors can be placed in line with PWM signals for servos. Cannot interfere with other robots, directly affect any output devices (e.g. generate PWM inputs for the Victor 884), be used for wireless communication or connect to the Radio or Tether Ports on the RC. | R03, R53, R64, R80-83 |  |
| 36 |  | No exposed electrical conductors and no electrical contact with robot metal chassis. No chassis parts used to carry electrical currents. Using an ohmmeter, confirm that the resistance between the chassis and each battery terminal is “large” (greater than 100k Ohms). | R51 |  |
| 37 |  | If decorations require electrical power, only the robot’s MK ES17-12 battery can be used. The decoration must be protected via either 20A or 30A circuit breaker and cannot interfere with other control system components. | R57 |  |

| PNEUMATIC SYSTEMS (if used) |
| --- |
| ITEM | PASS | DESCRIPTION | RULE(S) | COMMENTS |
| 38 |  | Acceptable Pneumatic Parts: refer to details in reference material | R01, R10, R35, R85-88, R92, R94 |  |
| 39 |  | Specifically Prohibited Pneumatic Parts: refer to details in reference material, confirm that the robot does not include any of the listed parts | R02, R89 |  |
| 40 |  | Must use the calibrated 125PSIG relief valve (without adjustments) on the compressor output and, if using an off-robot compressor, an additional valve must be located on the robot | R90, R94 |  |
| 41 |  | The manually operated pressure vent valve from the KOP must be present and easily accessible. | R90, R96 |  |
| 42 |  | Must include pressure gauges on the Clippard accumulator(s) and all regulator outputs. Must use the Norgren adjustable regulator at compressor output (“post-accumulator(s)”). | R90 |  |
| 43 |  | The Nason Co. pressure switch must be attached to the compressor output or Clippard tank(s) and be wired to the digital I/O port on the RC. The pressure switch CANNOT be used to directly power the compressor. | R90, R95 |  |
| 44 |  | No disallowed pneumatic component mods. Allowed mods include – cutting tubing, wiring for valves and pressure switch to accommodate interfacing to rest of system, the rear pin of air cylinders can be removed. | R91 |  |
| 45 |  | No extraneous tubing. | R01, R92 |  |
| 46 |  | If the robot design uses an “off-robot” air compressor, only the compressor and attached tubing can be located off the robot. The drive electronics, software, sensors and miscellaneous pneumatics elements must all be present on the robot as when using an “on-robot” air compressor. | R55, R93 |  |

| DRIVER CONSOLE AND POWER-UP |
| --- |
| ITEM | PASS | DESCRIPTION | RULE(S) | COMMENTS |
| 47 |  | OI/Driver Station console must fit on shelf that is 60” wide and 12” deep | R100 |  |
| 48 |  | Confirm that any device attached to the OI’s Dashboard Port is battery-powered (since there is no AC voltage available at the station) | R101 |  |
| 49 |  | OI indicator lights and ports must be visible and accessible. OI must be a 2008 model. | R98, R101 |  |
| 50 |  | Anything attached to the OI’s joystick ports (other than a USB-Chicklet from IFI) must derive power from the port. If a USB-Chicklet is used, it must be powered from a 7.2V battery pack similar to the back-up battery for the RC and the indicator lights must be visible. | R104-105 |  |
| 51 |  | Connect the OI to the tether port of the RC and power-up the robot. Confirm that the team number is properly displayed on the Operator Interface. Confirm that firmware version number 15 is being used. | R99 |  |
| 52 |  | Pneumatics Operational Test: If the robot design includes pneumatics, confirm that the pressure in the air storage tanks does not exceed 125PSIG, the “working” pressure does not exceed 60PSIG and confirm that the manually operated vent valve functions as required. | R90, R94-97 |  |
| 53 |  | While the robot is running, manually operate the 120A Main Breaker to disable the robot. Confirm that the RC has lost power (lights must go out) | R46, R50 |  |

Team Compliance Statement

We, the Team Mentor and Team Captain, attest by our signing below, that our team’s robot was built after the 2008 Kickoff on January 5, 2008 and in accordance with all of the 2008 FRC rules, including all Fabrication Schedule rules (reference Section 8.3.3).  We have conducted our own inspection and determined that our robot satisfies all of the 2008 FRC rules for robot design.

Team Captain:

Team Mentor: