# Hand Tools Training for the Moe Build Season

| COMPLETE |  |
| --- | --- |
|  | Hammer |
|  | Ball peen Use with center punch) |
|  | Soft face (plastic – non mark) |
|  | Lead (non mark steel) |
|  | Hacksaw |
|  | used to cut metal, plastic etc |
|  | Cuts on push stroke only – ease out on return – be deliberate in stroke |
|  | Use other hand on front of frame to guide |
|  | Teeth face forward |
|  | At least one tooth in work when cutting |
|  | Center Punch |
|  | Use to locate center of intended drilled hole |
|  | Has 90 in degree included angle (scribe is less) |
|  | Dial calipers |
|  | Measures thickness, diameter, Height |
|  | Measures in 1/1000 of an inch > called mils |
|  | range o to 6 inches |
|  | A piece of paper is about 3 mils or .003 inch |
|  | Scribe |
|  | Sharp point used to make lines on a layout |
|  | Deburring tool |
|  | Removes burrs on drilled holes or sharp edges. |
|  | Files |
|  | Must have a handle on them to use!!!!!! |
|  | cuts on forward stroke only |
|  | shapes flat round , triangular, square |
|  | use to deburr pieces |
|  | use a file card to clean the teeth out |
|  | Wrenches |
|  | Hex or Allen used on MOE (Bondus is special type or hex wrench) |
|  | open end wrench |
|  | Box |
|  | adjustable |
|  | Pliers |
|  | Needlenose |
|  | Vise grip locking |
|  | Water pump |
|  | cutting pliers > diagonal cutters “dikes” |
|  | Screwdrivers |
|  | standard spade “minus sign” |
|  | phillips “plus sign” |
|  | Sheet metal cutting |
|  | Tin snips |
|  | Aviation snips (right and left than cuts |
|  | Layout tools |
|  | Combination square |
|  | Scribe |
|  | Compass of circles |
|  | Straight edge |
|  | Tape Measure |
|  | Clamps |
|  | “C” clamp |
|  | Parallel Clamp |